## Slide 1
VillageConnect
Integrated Local Communication System
Connecting Rural Communities Without Internet
Project Team
Owais AbuSalah • Abdulah Dwekat • Anas Habash
Supervised by
Dr. Jihad Hamamra
Computer Networks Project • Academic Year 2025-2026

## Slide 2
The Challenge
Rural communities face a digital divide
No Internet Access
Remote areas lack reliable and affordable connectivity to the outside world.
Expensive Calls
Traditional phone services are costly and often unavailable in villages.
Poor Communication
No centralized system to share announcements or emergency alerts.
Limited Resources
Difficulty distributing educational materials to students and teachers.
Affecting over 3 billion people worldwide

## Slide 3
Our Solution
A complete self-contained network for the village
VillageConnect
Local network. Global features.
No internet required
Voice Calls (VoIP)
Free voice calls between all villagers using Asterisk PBX
Web Portal
Community announcements, directory, and news accessible via browser
File Sharing
Centralized educational resources, books, and videos for everyone

## Slide 4
Network Architecture
Three-tier hierarchical design for reliability and scalability
Core-Router
c3745
Core-Switch
VLAN Trunk
Village-Server
Ubuntu 24.04
Switch-Admin
VLAN 10
192.168.10.10
Switch-Public
VLAN 20
192.168.20.10
Switch-Voice
VLAN 30
192.168.30.10
CORE
DISTRIBUTION
ACCESS

## Slide 5
VLAN Segmentation
Logical separation of traffic for security and performance
10
VLAN
Admin
192.168.10.0/24
Village administration and council
~20 users
20
VLAN
Public
192.168.20.0/24
General community members
~900 users
30
VLAN
Voice
192.168.30.0/24
IP phones with QoS priority
~100 phones
40
VLAN
Servers
192.168.40.0/24
Backend services infrastructure
Ubuntu Server
All VLANs share the same physical network but are logically isolated through 802.1Q tagging

## Slide 6
OSPF Dynamic Routing
Open Shortest Path First — self-adapting inter-VLAN routing
Smart Routing
OSPF automatically calculates the best paths between all VLANs, adapting instantly to any topology changes.
Area 0
BACKBONE AREA
Fast Convergence
Networks converge in under 30 seconds after any topology change
Loop-Free
Dijkstra's Shortest Path First algorithm prevents routing loops
Scalable
Supports adding new VLANs and subnets without reconfiguration
Industry Standard
Widely used in enterprise networks worldwide (RFC 2328)

## Slide 7
Server Services
Three core services running on a single Ubuntu Server
VoIP Server
Asterisk PBX 20
Port 5060 (SIP)
5 extensions configured
Emergency calls (911)
Echo test (*43)
Announcements (100)
Web Portal
Apache Web Server
Port 80 (HTTP)
5 Arabic/RTL pages
Village announcements
Complete phone directory
Responsive design
File Sharing
Samba SMB/CIFS
Ports 139, 445
Public shared library
Upload folder for villagers
Admin-only secure area
Educational content

## Slide 8
Technologies & Tools
Built with industry-standard, open-source technologies
SIMULATION
GNS3
Network simulation platform
HARDWARE
Cisco IOS
c3745 Router & IOSvL2 Switches
VIRTUALIZATION
VMware
Virtualization for server
OPERATING SYSTEM
Ubuntu 24.04
Linux OS for the server
VOICE
Asterisk
Open-source VoIP PBX system
WEB
Apache HTTP
Web server for community portal
STORAGE
Samba
SMB/CIFS file sharing server
CLIENT
Twinkle
SIP softphone for testing

## Slide 9
Testing & Results
All network features verified successfully
100%
Tests Passed
<30s
OSPF Convergence
4
Active VLANs
5
VoIP Extensions
Test Results Summary
Test Case | Expected Result | Status
Ping PC-Admin to Gateway | Reply received | PASS
Inter-VLAN routing (all VLANs) | OSPF routes correctly | PASS
VoIP echo test (*43) | Voice echoed back | PASS
Web portal (Arabic RTL) | 5 pages load correctly | PASS
Samba file share access | Shares list and readable | PASS
SIP registration (Twinkle) | Registered with Asterisk | PASS

## Slide 10
Challenges & Solutions
Problems encountered during development and how we solved them
1
VMware-GNS3 Integration
PROBLEM
LAN Segments in VMware did not appear in GNS3 Cloud interfaces for bridging.
SOLUTION
Created VMnet2 in Virtual Network Editor (Host-only), linked Ubuntu VM to it, then selected VMnet2 in GNS3 Cloud configuration.
2
Reverse Path Filtering
PROBLEM
Ubuntu dropped packets coming from other VLANs, causing timeouts despite correct routing.
SOLUTION
Disabled rp_filter permanently in /etc/sysctl.conf, allowing Ubuntu to accept packets from any source subnet.
3
SIP Port Conflict
PROBLEM
Twinkle softphone could not bind to port 5060 because Asterisk was already using it.
SOLUTION
Configured Twinkle to use alternative port 5062 while Asterisk continued listening on standard port 5060.
4
Asterisk Authentication
PROBLEM
Linphone failed to register with 401 Unauthorized, not sending password credentials properly.
SOLUTION
Switched to Twinkle softphone which correctly handled SIP authentication and registered successfully.

## Slide 11
Live Demonstration
What you will see in our demo today
01
Network Topology
Live view of the complete network running in GNS3 with all devices operational
02
Inter-VLAN Ping Tests
Demonstrate OSPF routing between all four VLANs with successful ping replies
03
Arabic Web Portal
Browse the village website in Firefox showing all 5 pages with Arabic content
04
File Sharing (Samba)
Access the shared library and list educational content in the network
05
VoIP Call (*43)
Make an echo test call showing Asterisk is receiving and returning audio
06
Multi-Extension Calls
Show Admin (1000) and Mayor (1001) both registered and able to call each other

## Slide 12
Future Enhancements
Planned improvements and expansions for VillageConnect
WiFi Access Points
Wireless coverage for smartphones and tablets across the village
Video Conferencing
Jitsi Meet for online classes and remote medical consultations
Offline Content Cache
Pre-downloaded Wikipedia, Khan Academy for educational access
Mesh Networking
Extend coverage to remote areas using BATMAN-adv protocol
Solar Power
Self-sufficient network cabinets for areas with unstable electricity
Internet Backup
Optional satellite gateway for periodic external connectivity

## Slide 13
Meet the Team
The students behind VillageConnect
Owais AbuSalah
Network Design & Configuration
Abdulah Dwekat
Server & Services Setup
Anas Habash
Testing & Documentation
Supervised by
Dr. Jihad Hamamra

## Slide 14
Thank You
Questions & Discussion
VillageConnect
Connecting communities where internet cannot reach
Owais AbuSalah • Abdulah Dwekat • Anas Habash
Dr. Jihad Hamamra • Academic Year 2025-2026